|  | ......................... pc € .............................. € .............................. Panic lever lock set GEZE IQ lock EM able to be engaged at both sides Self-locking panic lever lock GEZE IQ lock EM for single leaf doors Changeover function for unlocking from the outside; integrated mechanical escape and child proofing to counteract misuse. Divided and separated cross latch for absolute unencumbered crossbar projection without jamming even when preloaded! The handle which can be electrically engaged on both sides (working current principle) allows unlocking from the outside and the inside. Daytime operation with permanently open position can be achieved through permanent coupling of the handles. Combines therefore well with access control systems. All required contacts are integrated in the lock and provide potential-free feedback: Deadbolt contact (with 95 % bolt throw) Handle contact (with handle activation on the panic side 10°) Cylinder contact Auxiliary lock contact (door open/door leaf enclosed) Release contact (exterior handle engaged) Prepared for installation of profile lock cylinders and with 9mm square nut. Closed and corrosion-resistant steel lock case in DIN sizes, front plate in stainless steel Nominal voltage: 24 V DC Current consumption: 210 mA Supplied in a set comprising: 1 pc lever mortise lock IQ lock EM with front metal plate 1 pc connecting cable 12-core; 10 m 1 pc cable duct open ( ) door leaf DIN right opening outwards / DIN left opening inwards ( ) door leaf DIN left opening outwards / DIN right opening inwards ( ) IQ lock EM 9235 (distance 92 mm, backset 35 mm) ( ) IQ lock EM 9240 (distance 92 mm, backset 40 mm) ( ) IQ lock EM 9245 (distance 92 mm, backset 45 mm) ( ) IQ lock EM 7255 (distance 72 mm, backset 55 mm) ( ) IQ lock EM 7265 (distance 72 mm, backset 65 mm) ( ) IQ lock EM 7280 special backset 80 mm ( ) IQ lock EM 7210 special backset 100 mm Accessories: ( ) 1 pc. power supply 24 V DC part no. 109637 ( ) 1 pc. GEZE panic bars (EN 1125) configurable part no. 119005 To ensure all functions of the IQ lock EM a door closer is to be fixed to the door. ( ) 1 pc. TS 5000 part no.027333 |
| --- | --- |