|  | ......................... Stk .............................. € .............................. € GEZE Levolan 60 sliding door fittings Sliding door fittings for leaf weights up to 60 kg - Clamping fittings for glass and wooden leaves, no leaf preparation necessary for installing the fittings - Smooth-running sliding door fittings, can be mounted from the front, tested in accordance with DIN EN 1527 - All fittings parts contained in the track with clip on cover - Complete overall height of fittings only 50 mm - Height adjustable +/- 3 mm using ex-centric cam incl. removal protection - Installation compensation against building tolerances +/- 3° - For glass panes made of ESG 8, 10, 12 mm as well as LSG up to 8.76 – 10.76 mm with LSG kit - Corrosion-proof components - Only one track for wall or ceiling installation - Fixed panel, glass and recessed ceiling installation - Bespoke, up to 6000 mm total track length Standard version (glass 1-leaf) wall / scope of supply: 1 track 1 cover profile 4 derailing protections 2 clamping roller carriages 6 cover brackets + 2 end stops 2 end covers for the track and cover profile 1 adjustable glass floor guide 8 – 13.5 mm Construction dimensions: Leaf width: .......................... mm Glass thickness: ................. mm Colour: ( ) EV1 ( ) stainless steel optic ( ) acc. to RAL Track length: ( ) 1650 mm ( ) 2050 mm ( ) 2450 mm ( ) Custom made, up to 6000 mm total track length Area of application: For single or double leaf sliding elements ( ) Levolan single leaf for wall installation ( ) Levolan single leaf for ceiling installation ( ) Levolan single leaf for ceiling installation with fixed panel ( ) Levolan single leaf for glass attachment ( ) Levolan double leaf for wall installation ( ) Levolan double leaf for ceiling installation ( ) Levolan double leaf for ceiling installation with fixed panel ( ) Levolan double leaf for glass attachment Accessories set Levolan SoftStop up to 60 kg leaf weight with adjustable trigger: ( ) Left, damped on one side ( ) Right, damped on one side ( ) Damped on both sides (Duo damper) |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Floor guide for glass leaf ( ) Floor guide for glass leaf (stainless steel) for 8, 10, 12 mm glass ( ) Continuous floor guide for glass leaf or floor guide for wooden leaf: ( ) Standard floor guide for wooden leaf |
|  | ......................... pcs. .............................. € .............................. € Additional buffer (floor or wall attachment) In addition to the end buffer, the door leaf must be stopped by a further buffer that is attached either at the middle of the door or at the bottom, so that the door leaf is stopped at the top and bottom at the same time. |
|  | ......................... pcs. .............................. € .............................. € GEZE modular fixed panel profile The GEZE fixed panel profile is suitable for bordering fanlights and side parts made of toughened safety glass and can be used as dry glazing for both internal and external applications. The system has been designed for glass thicknesses of 10 and 12 mm. The glass thicknesses are fixed with the identical clamping unit, there is no need for the system to be changed. The threaded nuts for the clamping units contained in the system can be positioned freely in the basic profile and set to the glass edge in accordance with the TRPV (Technical rules for the Design and Construction of Point-Supported Glazing by the German Centre of Competence for Construction). Additional drill holes related to the glass edges or clamping units are not required. The glass panes are set using system-compliant adjusting units which are integrated in the clamping unit and make a tolerance compensation of +/- 2.5 mm possible. Construction components from other manufacturers are not approved for adjustment. In addition, the clamping units can be extended using a safety set for freely suspended glazing. The basic system can be combined with different design clip-on covers. Basic system / basic profile ( ) Basic profile, aluminium, L = 6,000 mm ( ) Clamping system units, set 20 (20 pieces) adequate for a basic profile L = 6,000 mm, can be used for glass thicknesses of 12 mm Cover panels, design 40 aluminium (suitable for Glass Fittings, Perlan 140, Levolan etc.) ( ) Clip-on cover profile design 40 set for glass thicknesses of 10 to 12 mm (set = 2 profiles) ( ) Silver-coloured anodised surface ( ) Stainless steel colour anodised surface ( ) End cover cap for profile design 40 ( ) Silver-coloured anodised for glass thicknesses of 10 mm ( ) Silver-coloured anodised for glass thicknesses of 12 mm ( ) Stainless steel matt for glass thicknesses of 10 mm ( ) Stainless steel matt for glass thicknesses of 12 mm Optional accessories for the modular fixed panel profile ( ) Clamping system units, set 01 (1 piece) for additional clamping point ( ) Safety version set for fanlights and freely suspending glass panes, adequate for 5 clamping units |